## Slide 1
a
Preparation of the two circular Airy channels
CW
632.8 nm laser
SF
L₁
L₂
HWP
PBS₁
M₁
M₂
SLM₊
SLM₋
R₊
R₋
H
HWPᵢ
45°
HWPᵣ
45°
V
H
V
L₃
L₅
F₊: +1
F₋: +1
L₄
L₆
M₃
M₄
PBS₂
QWP
slow axis 45°
f
A
(r) exp[i(m − 1)φ]
f
A
(r) exp[i(m + 1)φ]
BS꜀
weak sample
output certification
QWP + LP: full Stokes
QWP + lens: spherical ref.
q
±
orthogonal circular
channels
free propagation
Carrier holograms (blazed gratings); F± pass +1, reject zero and other orders.
HWPᵢ / HWPᵣ align the SLM₋ input polarization and restore V before PBS₂.
Required: coaxial alignment, envelope / power balance and differential wavefront calibration.
Uniform relative phase leaves
I
±
and
S
3
unchanged.
x
z
y
select each circular channel
Notes: Source: Figure_S1_optical_layout.pdf, panel a.
Source: editable optical-layout deck with author-review corrections.
One proposed implementation is drawn: reflective phase-only LCOS-SLMs with a common working-axis orientation. The lower arm uses an HWP before modulation and a second HWP after its fold mirror to restore V at PBS2. Both arms retain Fourier-plane filtering. The drawing is schematic, with exaggerated incident/reflected separation; incidence angles and conjugate-plane distances are not specified.
Reflective phase modulation and polarization-axis alignment: Hamamatsu LCOS-SLM X15213 series, principle of modulation. https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/lpd/x15213_E.pdf
Circular-basis convention: e+ = (H+iV)/sqrt(2), e- = (H-iV)/sqrt(2). In the ideal model, the preparation QWP has its slow axis at +45 degrees and the analyzer QWP has its fast axis at +45 degrees. Circular-port signs must be calibrated, including any relay/mirror effects. Jones conventions: https://media.thorlabs.com/globalassets/family-pages/SharedAssets/p/po/Polarization_Handedness_Tutorial.pdf
Constant hologram/channel phases are adjusted to prepare the intended radial input, including compensation of fixed QWP/reflection phases. This does not imply a need for active phase locking of the intensity observable. main.tex lines 226-228: spatially uniform relative phase leaves I+/I- and S3 unchanged.
An output weak beam splitter supplies the prepared field for full-Stokes polarimetry and circular-channel reference interferometry. The reference wave is a separate unmodulated coherent reference combined in the certification module; the certification sample is not the unprepared PBS1 field.
P6 is handled by an output envelope/balance/wavefront calibration requirement, without specifying a flat-top shaping device or claiming achieved beam quality. Hardware model, retardance, optical tolerances, phase-only hologram encoding, intensity/charge/polarimetry certification and measurement precision remain experimental data required. The apparatus has not been built in this study (main.tex 874-876).
This is current Supplementary Fig. S1, as referenced in main.tex 865 and SI.tex figure experiment, not the earlier report label S6.
Zhu et al., Journal of Applied Physics 137, 223105 (2025), DOI 10.1063/5.0270605. Sec. III Eq. (5) and Fig. 2(b) include a blazed-grating carrier. Sec. IV and Fig. 3(a) use an L3-L4-aperture 4f system to isolate the +1 diffraction order. Here F+ and F- denote the two arm filters, and both pass their own +1 order; the arm signs are not diffraction-order signs. The polarizer P in Fig. 3 identifies polarization control. A two-SLM common-working-axis configuration is the present proposal, not their published apparatus. https://doi.org/10.1063/5.0270605 Primary article text accessed at https://www.researchgate.net/publication/392627647_Diverse_particle_manipulation_within_different_2D_planes_via_orientation-selective_Airy_vortex_beams
Liu et al., Nature Communications 12, 2230 (2021), DOI 10.1038/s41467-021-22462-z. Introduction separately discusses propagation of conventional different-charge beams and degradation from component misalignment. Our changing circular-channel profiles are part of the measured signal. The proposed interferometer requires common-axis registration, radial-envelope/power matching, and differential-wavefront calibration. No measured robustness is claimed, and the difference of two in charges is not evidence that alignment or aberration errors are negligible. https://www.nature.com/articles/s41467-021-22462-z Primary author manuscript: https://tsapps.nist.gov/publication/get_pdf.cfm?pub_id=930295
Yan et al., Photonics 12, 1029 (2025), DOI 10.3390/photonics12101029. Sec. 2.3 and Sec. 3 / Fig. 1 use a circularly polarized divergent spherical reference, produced by a QWP and lens, for coaxial interference to identify individual circular-component charges. The present certification module uses a weak sample of the prepared output, circular-channel selection, and a separately prepared mutually coherent reference from the same laser. The reference supply is a module input, not a sample of the prepared beam mistaken for an unmodulated reference. https://www.mdpi.com/2304-6732/12/10/1029 Primary article full text accessed at https://www.researchgate.net/publication/396644562_Vector_Vortex_Beams_Theory_Generation_and_Detection_of_Laguerre-Gaussian_and_Bessel-Gaussian_Types
Carrier selection is a proposal for generating the desired common complex envelope, not proof of achieved radial amplitude or phase fidelity. Fixed QWP/reflection phases must be calibrated for the intended input. Focal lengths, carrier periods, aperture sizes, coherence and charge-sign calibration remain device-specific requirements. The apparatus remains unbuilt.

## Slide 2
b
Simultaneous axial acquisition
plane z
relay L
BS
QWP
A
PBS₃
M₅
camera +
C
+
(x,y,z)
camera −
C
−
(x,y,z)
+
−
P
in
monitor
translated imaging head
Simultaneous full-frame counts; the moving ROI is applied digitally.
fast axis 45°
relative to PBS₃ H axis
Calibrate circular-port signs, gain and leakage.
Notes: Source: Figure_S1_optical_layout.pdf, panel b.
Analyzer QWP_A fast axis +45 degrees relative to PBS3 H transmission axis in the declared e+/e- convention. Ideally e+ maps to H (camera+) and e- to V (camera-). Actual port handedness is calibrated after the imaging relay and mirror train. https://media.thorlabs.com/globalassets/family-pages/SharedAssets/p/po/Polarization_Handedness_Tutorial.pdf

## Slide 3
c
From two count images to the axial event
raw counts
C
+
, C
−
+
−
dark / flat / gain
leakage
registration
same moving ROI
ρ ≤ ρ
s
(z)
Q = I
+
− I
−
T = I
+
+ I
−
p
3
= Q/T
Q = T
p
3
first stationary
peak + rising
half-height
z
50
(m)
Δz
m
=
z
50
(1) − z
50
(m)
Proxy:
x
s
= j′
m,1
; actual boundary: calibrated
S
3
= 0 contour.
The scan step sets axial sampling; uncertainty is obtained from
repeated calibrated count traces.
Apply the same event definition to every topological order.
Notes: Source: Figure_S1_optical_layout.pdf, panel c.